## Slide 2
Head Office:​
​
Erzbergerstr. 3 ​ 09116 Chemnitz, Germany
​
Phone: +49 371 9104-1 00​
Fax: +49 371 9104-105
​
info@kieselstein.com​
www.kieselstein.com ​

## Slide 3
Shaving Machines for Non-Ferrous Metals
Advantages
Technical Parameters
TECHNOLOGY – Reference Projects
Inlet wire diameter | max. 32.00 mm
Shaving speed | max. 10.00 m/s
Cutting depth (per side) | 0.01 mm – 0.50 mm
Compact design of the machines allows the integration into existing lines
Stand-alone coil to coil, coil to spool or spool to spool lines available
Full lines can be offered with different kinds of pay-offs as well as take-up systems
Double shaving as an option to increase the removal of material

## Slide 4
TECHNOLOGY – Reference Projects
Shaving Units for Large Range of applications
Inlet wire diameter | Max. 32.00 mm
Outlet wire diameter | Min. 0.80 mm
Cutting depth (per side) | 0.01 mm – 0.50 mm
Technical Parameters
Advantages
Large range of units
Design for all kinds of wire materials
Individual design for special requirements
Double shaving unit for maximum cutting depth
New design for non-ferrous with minimum distance for pointing and very compact design for a simple integration

## Slide 5
Aluminium Shaving Line
Reference Project:

## Slide 6
Reference Project:
Aluminium Shaving Line
Technological parameter:
Material: | Aluminium alloy (7050; 5056; 2117; 2017)
Diameter inlet wire: | max. 9.50 mm
Diameter finished wire: | min. 2.40 mm (in drawing process)
Block: | 2 pcs. (1x Drawing / 1x Shaving)
Drawing speed: | max. 180 m/min
Drawing capstan Ø: | 800 mm / Block
Manufacture option: | Coil to coil Coil to spool (Option)
Space requiered (LxBxH): | 27.000 mm x 9.000 mm x 5.200 mm

## Slide 7
Aluminium Shaving Line
Reference Project:
Structure:
Designation: | Coil pay-off ABV-T-Ueko
Function: | The pay-off device offers the flexibility to feed wire rings or coils into the system in an overhead process or tangentially with a rotary plate.

## Slide 8
Aluminium Shaving Line
Reference Project:
Structure:
Designation: | Draw Shaving line EHN 10/2
Function: | The wire is guided to the drawing block by a straightening device, positioned in front of the machine. In the first step, the wire is drawn on the block, which is equipped with a shedding ring. The shedding ring ensures, that the wire is drawn without damaging the surface.

## Slide 9
Aluminium Shaving Line
Reference Project:
Structure:
Designation: | Draw Shaving line EHN 10/2
Function: | In the second step, the shaving is done with the shaving unit DS-NE 150 positioned in front of the second block. The synchronisation of both blocks is done by a sensor roll. The unit can also be used for the pure drawing process.

## Slide 10
Aluminium Shaving Line
Reference Project:
Structure:
Designation: | String cleaning
Function: | Serves to clean the wire from lubricant residues (drawing and shaving emulsion).

## Slide 11
Aluminium Shaving Line
Reference Project:
Structure:
Designation: | Bending coiler BWV
Function: | Wire rings can be produced at a speed of up to 180 m/min. The rotating wire take-up supports the packaging in the line. The adjustable bending roller allows flexible adjustment of ring sizes.

## Slide 12
Aluminium Shaving Line
Reference Project:
Structure :
 | Further components: Spooling machine SH-Tr 1250 (Option – not yet included in the scope of supply) Drawing oil supply Cutting oil supply Chip conveyor

## Slide 13
Aluminium Shaving Line
Reference Project:
Why KIESELSTEIN?
Technologically mature holistic concept for the implementation of the shaving technology
Flexible production options:
Drawing with Shaving / Shaving /
winding on spools (optional) /
production of wire coils
Innovative ideas, for the further development of existing concepts

## Slide 14
THANK YOU VERY MUCH FOR YOUR ATTENTION!